## Slide 1: Revolution Robotics Foundation
Firmware upload with JFlash Lite

## Slide 2: Connecting the JLink Mini debugger
You have to connect debugger pins:
Pin 1 to TP17
Pin 2 to TP26
Pin 3 to TP23
Pin 4 to TP20
Pin 10 to TP29
Please note, that you can flash the MCU firmware only when MCU is powered on!

## Slide 3: Using JLink JFlash Lite
1) Install JLink_Windows_V644g.exe
2) Open JFlashLite.exe from C:\Program Files (x86)\SEGGER\JLink_V644g
3) Accept popup

## Slide 4: Flash MCU firmware with JFlash Lite I.
1) Select MCU type
2) Erase chip
3) Accept terms and conditions

## Slide 5: Flash MCU firmware with JFlash Lite II.
1) Browse our firmware
2) Program device
If connection to the target was successful, ERROR messages can be ignored.

## Slide 6: Using JLink command line tool for flashing
1) Install JLink_Windows_V644g.exe
2) Run our flashbl2.bat file (make sure that rrrc_bootloader.bin is next to the flashbl2.bat)

## Slide 7: Burn Raspberry PI TF card I.
Download etcher: https://www.balena.io/etcher/
Install etcher

## Slide 8: Burn Raspberry PI TF card II.
Select our image:
Select target TF card:
Press Flash!